## Slide 1: Town Lighting Review Policy
Lighting Standards & Sea Turtle Conservation

## Slide 2: Town Codes
LIGHTING STANDARDS
  Sec. 34-1831
  Purpose:
    curtail and reverse the degradation of the night-time visual environment
    minimize light pollution, glare, and light trespass
    conserve energy and resources
    maintain night-time safety, utility, security and productivity
  Applicability
    All new luminaires, regardless of whether a development order is required, must comply with the provisions and standards of this division

## Slide 3: Town Codes
Sea Turtle Conservation
  Sec. Sec. 32-101 to 102
  Purpose:
    protect nesting and hatchling sea turtles on the beaches in the Town
    ensure that nesting habitat is not degraded by artificial light
  Applicability
    all properties within the town that may produce artificial light directly, indirectly, or cumulatively visible from any portion of the beach, regardless of whether those properties are beachfront properties
    all buildings and related infrastructure, including landscaping, as well as all other activities that may adversely impact sea turtles

## Slide 4: Town Codes
When is a Lighting Review Required?
  Prior to issuance of development order or building permit for new structures, new construction, and improvements to existing structures for
    All structures waterward of 1991 CCCL
    All multi-family and commercial structures landward of 1991 CCCL

## Slide 5: Town Codes
When is a Lighting Review Required?
  Prior to issuance of development order or building permit for new structures, new construction, and improvements to existing structures for
    All structures waterward of 1991 CCCL
    All multi-family and commercial structures landward of 1991 CCCL

## Slide 6: What is a Lighting Review Reviewing?
  Light Standards (Sec. 34-1833)
    Illuminance = Brightness
      Photometric Data (Commercial & Multifamily (3+) Only)
      Must meet minimum and maximum standards
      Measured in Lumens, Footcandles, Watts
    Lamp Standards = Bulb/LED Type & Color
      Must be in harmony with the adjacent community
      Consistent with the task and setting
      Should not create a mix of colors

## Slide 7: What is a Lighting Review Reviewing?
  Light Standards (Sec. 34-1833)
    Luminaire Standards = Light Fixtures
      Fully shielded, full cutoff recessed bulbs and flat lenses are the only permitted fixtures for outdoor lighting
      Exceptions
        20 watt bulbs unshielded
        60 watt bulbs shielded
        Motion Detector Lights (must be properly configured)
        60 Watt Flood Lights (must be properly configured)
        All externally illuminated signs (shielded fixtures mounted at the top of the sign, aimed downward)
        Fixtures used to accent architectural features and landscaping

## Slide 8: What is a Lighting Review Reviewing?
  Light Standards (Sec. 34-1833)
    Mounting Standards = Light Poles
        Placement on Interior of Site Preferred
        15 Foot Mounting Height
          Except within 50 feet of Residentially Zoned = 12 Foot MH
          Exception for existing poles
        Building Mounted
          Must be attached to walls
          MH may not exceed lowest point of roof or parapet
        Canopy Lighting
          Must be fully shielded full cutoff fixtures

## Slide 9: What is a Lighting Review Reviewing?
  Light Standards (Sec. 34-1833)
    When specific standards are not addressed in these sources, the standards of the Illuminating Engineering Society of North America (IESNA) will apply
    In addition to the standards and criteria in this section, there are standards for artificial lighting near sea turtle nesting habitat
    = Sea Turtle Conservation Code

## Slide 10: What is a Lighting Review Reviewing?
  Sea Turtle Conservation Code (Sec. 32-105)
    All artificial lighting affixed to the exterior of new permanent structures, construction or additions shall be:
      long wavelength
      downward directed
      full cutoff
      fully shielded (exception for lights on landward side of building)
      mounted as close to the ground as possible
      Must achieve required foot candles
        Florida Building Code
        Department of Health

## Slide 11: Why do we need lighting reviews?
  Human Health and Safety
    Not too Bright, Not too Dark
    Not subjective - Use Illuminance Guidelines in Code
  Sea Turtle Conservation
    Increase hatchling survival rates for species recovery
    Sea Turtles are natural light detectors

## Slide 12: What happens when we do not review lighting?

## Slide 13: Existing Lights Reviewed?
  Requested to be included in Lighting Plan submittal
  Not always in scope of project to be review-able
  Just replacing lights that were here before…
  What does Code Say?
    Sec. 34-1834 (c) Existing light fixtures must be brought into compliance with this code by January 1, 2010.
    Any fixtures replaced after the date of the adoption of this code must be replaced with fixtures that comply with the standards established herein.
    Illuminance levels specified in this code apply to all outdoor lighting.
    Sec. 32-106. Existing artificial lighting affixed to the exterior of permanent structures shall not be directly, indirectly, or cumulatively visible from any portion of the beach during sea turtle nesting season.

## Slide 14: What is TFMB Policy?
Directly visible from the Beach
  Long wavelength light source
  In downward directed fixture
  Light source is shielded from the beach
  Includes structures that are NOT beach front
    Why?
    Hurricane Ian removed vegetation and structures that previously shielded light
    View corridors must be assessed 270 degrees from source
      Estero Island is S-shaped
      Lights can be visible from multiple angles
    Can be visible from other beaches!

## Slide 15: What is TFMB Policy?
Indirectly visible from the Beach
  Long wavelength light source
  Not required to be shielded provided light is not directly, indirectly, or cumulatively visible from any portion of the beach
  Must still comply with Light Standards Code

## Slide 16: What is TFMB Policy?
Cumulatively visible from the Beach
  What does that even mean???
  Sec. 32-103 Cumulatively visible means light from numerous artificial light sources on a single property that as a group are directly or indirectly visible to an observer standing anywhere on the beach.
  How do we assess this?
  Where does indirectly visible end and cumulatively visible begin?
  In other words, where do we stop requiring long wavelength lights and only require Lighting Standards Code to apply?

## Slide 17: What is TFMB Policy?
Options
  Require Long Wavelength Light Everywhere?
  Use 1991 CCCL as delineation?
  Use FWC Guidance?

## Slide 18: What is TFMB Policy?
Created by the FWC's Imperiled Species Management Section.
Buffers are for planning purposes only and includes the minimum recommended area where specific lighting should occur.
Wildlife-Sensitive Conventional Lighting (RED LAYER)
  minimum recommended area where lighting should be designed to meet the criteria for Wildlife-Sensitive Conventional Lighting
Dark Sky (GREY LAYER)
  minimum recommended area where lighting should be designed to minimize glare and sky glow by using downward directed, full cut off fixtures.

## Slide 19: What is TFMB Policy?